## Slide 1: Breakout game with controller using Matter over Thread
By Bart Gysen

## Slide 2: Goals
Knowledge
Demo

## Slide 3: Contents
Project overview
Matter
OpenThread
Game controller
Matter controller
Breakout game
Q&A

## Slide 4: Project overview
Matter demo
Breakout game
Controlled with motion

## Slide 5: Matter - contents
About
Architecture
Data Model
Interaction Model
Network
Security
Commissioning
Hub & Bridge
CSA membership & certification
Develop with Matter

## Slide 6: Matter - About
Open source connectivity standard for the smart home
Connectivity Standards Alliance
Connected Home over IP (CHIP)
interoperability and compatibility
Reliability
Secure
First official release V1.0 in September 2022
Release V1.1 in May 2023 – bug fixes and SDK improvements
Release V1.2 in October 2023 – expanding with new device types
Notes: CSA formerly Zigbee Alliance Rebranding in 2021

## Slide 8: Matter – Architecture
Notes: Application layer TCP/IP mode

## Slide 9: Matter – Architecture
STUDY THIS!!!!!
Notes: Divided into layers

## Slide 10: Matter – Data Model - Concept
Hierarchical model
Device features

## Slide 11: Matter – Data Model - Node
Uniquely addressable entity
One or more endpoints
Set of behaviors
  Dimmable Light
  Dimmer Switch

## Slide 12: Matter – Data Model - Endpoint
Set of functionality’s
  On/Off
  Level Control
Contains clusters

## Slide 13: Matter – Data Model - Cluster
Reusable building blocks
Grouping commonly used functionality
Application cluster specification

## Slide 14: Matter – Data Model – Device Type
Officially defined collection of requirements
Intended to ensure interoperability
Device library specification

## Slide 15: Matter – Data Model – Custom Cluster
Designed to add functionalities
Reusing or extending a existing cluster will only work with custom controller
A new cluster specification only possible with a least an adoption-level member
Notes: Put it in the explanation of the game controller.

## Slide 16: Matter – Interaction Model
Defines the methods of communication
Initiators - Targets
Notes: Every interaction except Subscribe consists of one transaction

## Slide 17: Matter – Interaction Model – Read
Get attributes and/or events
Restricted to unicast
Initiator requests a list of attributes and/or events
Target responds with requested list and a suppress response flag
Initiator generates a status response, not send when suppress response flag is set

## Slide 18: Matter – Interaction Model - Write
Modify values of attributes
Untimed or Timed transaction
Untimed two actions
Timed four actions
Notes: Write action = Write request, Timed Request, Suppress Response flag

## Slide 19: Matter – Interaction Model - Invoke
To invoke commands
Similar to write interaction
Untimed / Timed
Notes: Used for e.g. By the controller to invoke one of the commands of the data link layer.

## Slide 20: Matter – Interaction Model - Subscribe
Used to automatically receive updates
Restricted to unicast
Will be checked with status and subscribe response

## Slide 21: Matter – Network
IPv6
Focus on three link layer technologies
Single Network Topology
Star Network Topology
Notes: The Matter protocol can operate without a globally-routable IPv6 infrastructure and allows the flexibility of having multiple Matter networks run over the same set of constituent IP Networks.

## Slide 22: Matter – Network – Single Network Topology

## Slide 23: Matter – Network – Star Network Topology

## Slide 24: Matter - Commissioning
Pairing method
Performed over BLE
Controller needs onboarding payload:
  QR Code
  QR Code Payload used in command line tools
  Manual pairing code
Security steps

## Slide 25: Matter - Commissioning

## Slide 26: Matter – Fabric
The whole network
Sharing the same security domain

## Slide 27: Matter – Multiple Fabrics
Notes: Specification

## Slide 28: Matter – Hub & Bridge
Hub
Serves as controller
Not tied to ecosystem
Often functions as Border Router
Bridge
Add more flexibility
Acts as translator for non-Matter devices

## Slide 29: Matter – CSA Membership & certification
Membership necessary for certifying
Official resources
Authorization to contribute
Unique Vendor ID

## Slide 31: Matter – Develop with Matter
GitHub project-chip
  SDK
  Documentation
  Certification tool
Manufacturer SDK
  Manufacturer IDE
  A lot of examples you can use

## Slide 32: OpenThread
Mesh Network-protocol
IEEE 802.15.4
IPv6
Low-power
Border Router
Notes: Institute of Electrical and Electronics Engineers

## Slide 33: Game Controller
EFR32MG24 SoC - BRD2601B All-in-one-Solution
No device type available
To make it work, the protocol is abused
Consideration Client vs. Server

## Slide 34: Matter Controller
Raspberry Pi 4
Radio Co-Processor EFR32xG21
Ubuntu with CHIP-Tool and OpenThread
Python Breakout game
Notes: RCP omdat dit de main processor ontlast.

## Slide 35: Breakout game
Using CHIP-Tool to interact

## Slide 36: Q&A